## Slide 1: Concrete Strength Prediction
Mark Gregory & Abel Berta

## Slide 2: Why This Matters
We predict compressive strength, measured in megaparsec (MPa).
Overestimating strength could lead to unsafe mix decisions.
Underestimating strength can cause over-design, higher material cost, and unnecessary cement use.
A useful model can help narrow candidate mixes before full lab validation

## Slide 3: Data Overview
Source: UCI Concrete Compressive Strength dataset.
Raw data: 1,030 rows × 9 columns.
Predictors: 8 mix/curing variables — cement, slag, fly ash, water, superplasticizer, coarse aggregate, fine aggregate, age.
Target: concrete compressive strength in MPa.
After removing 25 duplicate rows, modeling used 1,005 rows.
Train/test split: 804 train / 201 test using an 80/20 split.

## Slide 4: Target Distribution
Strength range: 2.33 to 82.60 MPa.
Mean strength: 35.82 MPa.
Median strength: 34.44 MPa.
Distribution is mildly right-skewed, with some very low and very high strength values.

## Slide 5: Key EDA Patterns
Strongest positive raw correlation: cement, r = 0.50.
Other positive relationships: superplasticizer, r = 0.37; age, r = 0.33.
Strongest negative raw relationship: water, r = −0.29.
This matches concrete-domain intuition: more binder/curing improves strength, while excess water weakens the mix.

## Slide 6: Preprocessing Decisions
Removed 25 duplicate rows before modeling.
No missing target values: 0 missing target rows.
No missing predictor values in train or test: 0 missing feature values.
Used an 80/20 train-test split with random_state = 4950.
Applied IQR outlier capping using training data only.
Largest outlier rate was Age: 6.09%; water and superplasticizer were also capped.

## Slide 7: Feature Engineering
Started with 8 raw predictors.
Engineered 40 features, then pruned to 29 retained features.
Best engineered correlations with strength:
  binder_x_age: r = 0.821
  cement_x_age: r = 0.731
  binder_minus_water: r = 0.636
Engineered + StandardScaler improved CV RMSE from 8.36 MPa to 6.36 MPa in Ridge-style validation.

## Slide 8: Models Trained
Baseline: predict the training mean every time.
Linear models: Linear Regression, Ridge, Lasso.
Tree models: Decision Tree, Random Forest, Gradient Boosting.
Tuned models: Ridge, Random Forest, Gradient Boosting.
Validation: held-out test set plus 5-fold cross-validation.

## Slide 9: Model Comparison
Naive baseline RMSE: 15.71 MPa.
Best model: Tuned Gradient Boosting.
Tuned Gradient Boosting test RMSE: 4.0616 MPa.
Tuned Gradient Boosting test R²: 0.9331.
Tuned Gradient Boosting reduced RMSE by about 11.64 MPa versus the naive baseline.

## Slide 10: Test Performance and Cross-Validation
Best hyperparameters: learning rate 0.1, max depth 3, estimators 300.
5-fold CV mean R²: 0.9230.
5-fold CV standard deviation: 0.0192.
Train R²: 0.9873; test R²: 0.9331.
Train-test R² gap: ~0.0542.

## Slide 11: Error Analysis
Test RMSE = 4.0616 MPa, much lower than baseline RMSE = 15.71 Mpa.
.Actual vs. predicted points mostly follow the diagonal, showing strong overall fit.
Residuals are centered near zero: mean residual = 0.13 MPa, suggesting little overall bias.
Main risk: a few high-error mixes remain, especially at moderate-to-high predicted strengths.

## Slide 12: Feature Importance
Top feature: binder_x_age, importance 0.523.
Second: water_binder_ratio, importance 0.166.
Third: cement_x_age, importance 0.147.
Interpretation: strength depends most on cementitious material, curing time, and water relative to binder.

## Slide 13
Recommendations, Limitations, and Next Steps
Use the model to screen mixes, not replace testing
Recommendations
Use the model for early mix screening because it cuts RMSE from 15.71 MPa to 4.0616 MPa.
Use binder-age balance as a key screening signal when comparing candidate mixes.
Monitor water-binder ratio carefully; it was the second-most important feature with importance 0.166.
Limitations
Dataset is modest: 1,005 cleaned rows from a public dataset, not local production data.
Missing real-world variables such as curing temperature, humidity, material cost, cement type, and site conditions.
Next step
Validate the model on local/project-specific concrete batches and add cost and environmental impact data.